## Slide 1: INTRODUCTION OF WAVEGUIDES
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Prepared by
RAADHU.T
ASSISTANT PROFESSOR

## Slide 2: INTRODUCTION OF WAVEGUIDES
1

## Slide 3
INTRODUCTION TO WAVEGUIDES
In a waveguide energy is transmitted in the form
of electromagnetic waves whereas in transmission line, it is transmitted in the form of voltage and current.
Conduction of energy takes place not through the walls whose function is only to confine this energy but through the dielectric filling the waveguide which is usually air.
ADVANTAGES OF WAVEGUIDE OVER A TRANSMISSION LINE :
In a transmission line high frequency signals cannot be transmitted because
  Large mutual induction.
  Length is very large.
Multiplexing the signals is not possible in transmission lines.
Flashover is less in case of waveguide.
Minimum loss of power in case of waveguide.
Power handling capability is 10 times than coaxial cable.
3

## Slide 4
REFLECTION OF WAVEFORM IN CONDUCTING PLANE :
INTRODUCTION TO WAVEGUIDES
Mechanical simplicity.
Higher maximum operating frequency.(3GHZ to 100GHZ).
Normally waveguides are of two types.
  Rectangular waveguide.
  Circular waveguide.
a
b
Rectangular waveguide
d
Circular waveguide
Vg
4
VR
Vn
VI
V is velocity guided by wall
g
(group velocity)
Vn is the normal velocity to wall

## Slide 5
a
L
DOMINANT MODE OF OPERATION
DOMINANT MODE : The natural mode of oper-
-ation for a waveguide is called dominant mode. This mode is the lowest possible frequency that can be propagated in a waveguide.
a
L
L
a
ELECTRIC FIELD
>
>
>
MAGNETIC FIELD
5
m=no. of half wavelength across waveguide.
n=no. of half wavelength along the waveguide height.

## Slide 6
DOMINANT MODE OF OPERATION cont …
n=1 => 1 circle n=2 => 2 circles
m- electric field
n – magnetic field
Magnetic field
m=1 m=2
6
The signal of maximum wavelength that can pass through a waveguide is
λ0=2a/m
BASIC BEHAVIOUR
An electromagnetic plane wave in space is transverse electrom- agnetic or TEM. The electric field, the magnetic field and direction of propagation are mutually perpendicular. If such a wave were sent straight down a waveguide, it would not propagate in it. This is because the electric field would be
short-circuited by the walls since the walls are assumed to be

## Slide 7: Perfect conductors and a potential cannot exist across them.
BASIC BEHAVIOUR cont….
What must be found in some method of propagation which doesn’t require an electric field to exist near a wall and simultaneously the parallel to it. This is achieved by sending the wave down the waveguide in a zigzag fashion bouncing it off the walls and setting of a field i.e., maxima at the centre of waveguide and zero at the walls.
In this case, the walls are nothing to be short circuit and they
don’t interfere with the wave pattern setup between them.
To measure consequences of zigzag propagation are apparent. The first is that velocity of propagation in a waveguide must be less than that of free space.
7

## Slide 8
PLANE WAVE OF A CONDUCTING SURFACE
If actual velocity of wave is Vc , then the simple trigonometry shows that the velocity of the wave in the direction parallel to conducting is Vg and velocity normal to the wall is Vn.
Vg
V
n
VC
λP
λ
λ
n
θ
PARALLEL AND NORMAL WAVE LENGTH: Distance between 2 successive identical points i.e., successive crests or successive troughs. In the figure, it is seen that the wavelength in direction of propagation of wave is λ being the distance between 2 successive crests in this direction.
INCIDENT WAVE
8
REFLECTED
WAVE

## Slide 9
p
PARALLEL AND NORMAL WAVELENGTH cont….
So the distance between 2 consecutive crests in
the direction parallel to conducting plane is λp and wavelength perpendicular to surface is λn.
λ = λ λn = λ
sinθ cosθ
VC = f λ
Vg = VC sinθ
sinθ
Vp= fλp= f λ =
V
C
sinθ
Vp – phase velocity – velocity with which wave changes its phase. Vg – group velocity – velocity parallel to wall.
PARALLEL PLANE WAVEGUIDE
In order to wave to propagate in a waveguide there should be no voltage at the walls because walls are purely conductive if there exists some voltage at walls the wave get shorted and there will be no propagation of wave.
Eq 1
VNIT

## Slide 10
PARALLEL PLANE WAVEGUIDE cont…..
Voltage variation in waveguide is almost similar to the transmission lines.
Waveform of voltage in transmission lines is as follows
λ/2
2λ/2
3λ/2
So dimension of waveguide can have following values such that voltage at walls will be zero.
a= λn / 2
a=2 λn / 2
a=3 λn / 2

## Slide 11
DERIVATION OF CUT OFF WAVELENGTH
‘a’ is the distance between the walls λn is the wavelength in the direction normal to both walls.
‘m‘ is the no .of half wavelength of electric intensity to be
established between walls which is nothing but integer.
From equation , it is easy to say that as the free space wave length is increased, there comes a point beyond which, the wave can no linger propagate in a waveguide with fixed ‘a’ & ‘m’ . The free space wavelength at which this takes place is called cut off wavelength and it defines as the smallest free
2
a = mλn = mλ
2cosθ
From Eq 1
mλ
cosθ = 2a
P
sinθ
√ 1- cos2 θ
λ = λ = λ λ
√ 1- (mλ)2
(2a)2

## Slide 12
DERIVATION OF CUT OFF WAVELENGTH
Space wavelength that is just unable to propagate in waveguide under such condition.
1-
So a waveguide allows a signal having a frequency more than cut off frequency so a waveguide acts as high pass filter.
The lowest cut off frequency can be calculated through
mλo
2a
( )
2
=
0
o
λ =
2a
m
λo= cut off wavelength for dominant mode , m=1 , λo=2a
λ
λp = √ 1 - λ( m )2
λp =
2a
λ
o
√ 1 -( λ )
λ 2
λp = guided wavelength
λ = free space wavelength
fc =1.5*10
8
√
m
a
(
)
2
+
(
n 2
b )

## Slide 13
PROBLEM
Calculate the lowest frequency and determine
the mode closest to the dominant mode of rectangular waveguide 5.1cm*2.4cm.Calculate the cut off frequency of dominant mode?
Ans) From the formula in previous slide for dominant mode is TE1,0 so m=1,n=0,a=5.1*10-2 ,b=2.4*10-2 we get
fc = 2.94GHz
Mode closest to dominant mode can be determined by substituting m , n values.
for m=0, n=1, we get fc = 6.25GHz for m=0, n=2, we get fc = 12.5GHz for m=2, n=0, we get fc = 5.8GHz
As fc = 5.8GHz in TE2,0 is close to fc= 2.94GHz in TE2,0 , therefore
mode closest to dominant mode is TE2,0 .

## Slide 14
GROUP AND PHASE VELOCITY IN WAVEGUIDE
g c p
V = V sinθ V =
Vp Vg = (Vc )2 ------Eq 2
Vp=f λp
p
Substituting above equation in Eq 2 we get
Vg = Vc
The above equation represents that velocity of propagation or group velocity in a waveguide is lower than in free space. Group velocity decreases as the free space wavelength approaches the cut off wavelength and is zero when the two wavelength are equal.
sinθ
V
c
θ
Vg
Vc
Vn
θ
λp
λ
λn
V =f λ
√
1 -
(
λ
λo
)2
Vp=
Vc
1 -
λ
√ ( )
λo
2
(
√
1-
λ
λo
2
( ) )

## Slide 15
PROBLEM
It is necessary to propagate a 10GHz signal in a
waveguide whose wall separation is 6cm.What is the greatest no.of halfwaves of electric intensity which it will possible to establish between 2 walls. Calculate the guide wavelength for this mode of operation?
Solution:
a = 6 cm , f = 10GHz => λ = f/c = 3cm
λ0 = (2*a)/m
for m=1 => λ0 =12/1 =12 cm for m=2 => λ0 =12/2 =6 cm
for m=3 => λ0 =12/3 =4 cm
for m=4 => λ0 =12/4 =3 cm
So maximum value of m is 4.